## Slide 1: Logic Gates The Basic Gates and Circuits
Notes: TES

## Slide 2: Recall
Add the following Binary numbers:
10101111 + 10110111

## Slide 3: Recall
Multiply the following binary number by 2. (Hint: Logical binary shift)
10110111

## Slide 4: Lesson Objectives
Understand the functions of the main logic gates
Know how to design simple circuits using logic gates
Understand how to construct a Truth Table for simple logic circuits

## Slide 5: Logic Gates
A logic gate is a digital circuit which either allows a signal to pass or stops it
Logic gates allow the computer to:
Add
Divide
Multiply
Do simple Yes and No reasoning

## Slide 6: Overview
There are six basic logic gates: AND, OR, NOT, NAND, NOR, and XOR
AND GATE
NOT GATE
OR GATE

## Slide 7
NOT
AND
OR
Exclusive OR

## Slide 8: Truth Tables
Every Logic Gate has a Truth Table to describe the output of a particular Boolean logic operation.
A | B | Y
Inputs and outputs
are labelled
There are two inputs giving four possible values
0
0
0
0
1
1
1
1

## Slide 9: AND Gates
Gives a TRUE result (1) if both inputs are TRUE (1)
A | B | Y = A AND B
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
A
Y
B
0
0
0
1

## Slide 10: OR Gates
A | B | Y = A OR B
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
Gives a TRUE result (1) if any input value is TRUE (1)
A
B
Y
0
1
1
1

## Slide 11: NOT Gates
Changes the input value to its opposite value
This Logic Gate only has one input
A | Y = NOT A
0 | 
1 | 
Y
A
0
1

## Slide 12: NAND Gates
Gives an output of 1 if both input values are NOT 1 (the opposite of an AND Gate)
A | B | A NAND B
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
A
Y
B
0
1
1
1

## Slide 13: NOR Gates
Gives an output of 1 if both the inputs are 0 (the opposite of an OR Gate
A | B | A NOR B
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
A
Y
B
0
0
0
1

## Slide 14: XOR Gates
Gives an output of 1 if the two input values are different
A | B | A XOR B
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
A
Y
B
0
1
1
0

## Slide 16: Summary
Name | Symbol | Description
NAND Gate
AND Gate
OR Gate
NOR Gate
NOT Gate
XOR Gate
Reverses the input
Also known as an inverter gate
Exclusive OR gate - Output is only 1 if either input is 1.
If both inputs are 1, the output is 0
NOT-OR Gate – Opposite of OR Gate
Output is 1 only if both inputs are 0
Output is 1 if either input is 1
Output is 0 only if both inputs are 0
NOT-AND Gate – Opposite of AND Gate.
Output is 1 only if any input is NOT 1
Output is 1 only if all inputs are 1
Notes: Optional Retrieval Practice – print from last section of this presentation

## Slide 17: Produce a Truth Table for the following logic circuit
A
B
C
X
P
Q
R

## Slide 18
Input Value |  |  | Intermediate Values |  |  | Output
A | B | C | P | Q | R | X
0 | 0 | 0 |  |  |  | 
0 | 0 | 1 |  |  |  | 
0 | 1 | 0 |  |  |  | 
0 | 1 | 1 |  |  |  | 
1 | 0 | 0 |  |  |  | 
1 | 0 | 1 |  |  |  | 
1 | 1 | 0 |  |  |  | 
1 | 1 | 1 |  |  |  | 

## Slide 19
Input Value |  |  | Intermediate Values |  |  | Output
A | B | C | P | Q | R | X
0 | 0 | 0 |  |  |  | 
0 | 0 | 1 |  |  |  | 
0 | 1 | 0 |  |  |  | 
0 | 1 | 1 |  |  |  | 
1 | 0 | 0 |  |  |  | 
1 | 0 | 1 |  |  |  | 
1 | 1 | 0 |  |  |  | 
1 | 1 | 1 |  |  |  | 
P = A AND B
0
0
0
0
0
0
1
1
Q = B NOR C
1
0
0
0
1
0
0
0

## Slide 20: R = P OR Q
Input Value |  |  | Intermediate Values |  |  | Output
A | B | C | P | Q | R | X
0 | 0 | 0 |  |  |  | 
0 | 0 | 1 |  |  |  | 
0 | 1 | 0 |  |  |  | 
0 | 1 | 1 |  |  |  | 
1 | 0 | 0 |  |  |  | 
1 | 0 | 1 |  |  |  | 
1 | 1 | 0 |  |  |  | 
1 | 1 | 1 |  |  |  | 
0
0
0
0
0
0
1
1
1
0
0
0
1
0
0
0
1
1
1
1
0
0
0
0
X = C XOR R
1
1
1
1
1
0
1
0

## Slide 21: Exercise One
C
D
E
A
B
X
Notes: 3.12 a

## Slide 22: Exercise One – Truth Table
Input Value |  | Intermediate Values |  |  | Output
A | B | C | D | E | X
0 | 0 |  |  |  | 
0 | 1 |  |  |  | 
1 | 0 |  |  |  | 
1 | 1 |  |  |  | 
0
0
0
1
0
1
1
1
1
0
0
0
1
1
0
0

## Slide 23: Exercise Two
Notes: 3.2 b

## Slide 24: Exercise Two – Truth Table
Input Value |  | Intermediate Values |  |  |  | Output
A | B |  |  |  |  | X
0 | 0 |  |  |  |  | 
0 | 1 |  |  |  |  | 
1 | 0 |  |  |  |  | 
1 | 1 |  |  |  |  | 
C
D
E
F
1
1
0
0
0
1
1
1
0
1
0
0
1
1
1
1
1
0
1
1

## Slide 25: Exercise Three
D
E
F
A
B
C
X
Notes: Teach need to labl the intermediate points

## Slide 26: Exercise Three – Truth Table
Input Value |  |  | Intermediate Values |  |  | Output
A | B | C |  |  |  | X
0 | 0 | 0 |  |  |  | 
0 | 0 | 1 |  |  |  | 
0 | 1 | 0 |  |  |  | 
0 | 1 | 1 |  |  |  | 
1 | 0 | 0 |  |  |  | 
1 | 0 | 1 |  |  |  | 
1 | 1 | 0 |  |  |  | 
1 | 1 | 1 |  |  |  | 
D
E
F
0
0
1
1
1
1
1
0
1
1
0
1
1
1
1
0
1
1
1
1
0
1
1
0
1
1
1
0
0
0
0
1

## Slide 27: Exercise Four
D
E
F
G
A
B
C
X

## Slide 28: Exercise Four – Truth Table
Input Value |  |  | Intermediate Values |  |  |  | Output
A | B | C |  |  |  |  | X
0 | 0 | 0 |  |  |  |  | 
0 | 0 | 1 |  |  |  |  | 
0 | 1 | 0 |  |  |  |  | 
0 | 1 | 1 |  |  |  |  | 
1 | 0 | 0 |  |  |  |  | 
1 | 0 | 1 |  |  |  |  | 
1 | 1 | 0 |  |  |  |  | 
1 | 1 | 1 |  |  |  |  | 
D
E
F
0
0
1
1
1
0
0
0
1
1
0
0
0
1
0
0
1
1
1
1
1
1
1
0
1
0
0
0
0
0
0
0
0
1
0
0
1
0
0
0
G

## Slide 29: Exercise Five - Tricky Question?
A
B
X
What Gate does this circuit produce? [1]
[2]
OR Gate

## Slide 30: Summary
Name | Symbol | Description
NAND Gate
AND Gate
OR Gate
NOR Gate
NOT Gate
XOR Gate
Notes: Optional Retrieval Practice

## Slide 31: Exercise One
C
D
E
A
B
X
Notes: 3.12 a

## Slide 32: Exercise Two
C
D
E
F
A
B
X
Notes: 3.2 b

## Slide 33: Exercise Three
D
E
F
A
B
C
Notes: 3.2 c

## Slide 34: Exercise Four
D
E
F
G
A
B
C