## Slide 1
YEAR 9 GRAPHICS KNOWLEDGE ORGANISER – MRS YOUNG
A
Paper/ Board | Properties | Common uses
Bleed proof | Smooth paper, often used with water and spirit based markers Prevents marker bleed (when ink runs and seeps through paper) | Used for presentation drawings
Cartridge paper | Good Quality white paper often with a slight texture Available in different weights | Due to the good-quality surface, it can be used for paints and markers as well as drawing
Grid | Paper printed with different grids a guidelines (these can be isometric or differently sized grids.) | Quick model making and working drawings
Layout paper | Thin transparent light weight paper Can be drawn on with markers and takes colours well | Initial quick sketching and tracing
Tracing paper | Thin transparent paper | Tracing copies of drawings
Duplex Board | Thin board which often has one side that is suitable for printing | Used for food packaging Can be easily recycled
Corrugated board | Strong, light weight material. Made up of two or more layers and a fluted middle section leading to good instating properties. Available in different thicknesses | Used for packaging such as pizza boxes and large boxes for heavy items that need protecting.
Foil-lined board | White card coated or laminated with aluminium foil bonded onto one side. It has moisture and thermal retention properties | It is used for drinks cartons & takeaway containers.
Foam-core board | Foamcore, foam board, or paper-faced foam board is a lightweight and easily cut material. | Used for mounting photographs and for making scale models
Laminated paper | Paper layered sheets of clear plastic over it, to improve the durability of it. | Wide range of uses where protecting the paper from moisture or wear is needed
Inkjet card | Treated so it can be used in all inkjet printers | Printing on inkjet printers
Solid white board | Top quality cardboard, smooth and white Good for printing on. | Book covers
B
C
Embossing the design is raised by pushing the material upwards from the back.
Debossing the design is pressed into the surface from the front.
Foil blocking a heated die applies a foil to the surface of the material for a high end finish.
D
E
F
SRA sizes of paper are slightly larger than ‘A’ sizes to allow for a bleed area in printing.
Off Set Lithography
CMYK – Cyan, Magenta, Yellow and Black
Die cutting cuts and deforms the material for easy folding, deforming is better than scoring as the material is compressed not cut making it stronger.